BALE-PAK BP 120/P Fully automatic 30-45 KW POLYBALERS

METHOD OF OPERATION

Shavings are fed to the machine by means of the Feed Hopper provided.  This is normally extended by several metres when installed to give a reasonably large storage area above. This will cope with local surges and smooth out the feed rate to the Baler.

Each bale is made by one stroke of the compression ram, which is activated by an Infrared sensing device in the Hopper. When this ram has reached the fully forward position (bale fully compressed) the gate on the baler will open allowing the long eject cylinder to eject the compressed bale out of the bagging spout.  This will only happen provided the sealing unit on the machine is activated and the polythene roll has been placed in the machine wrapped around the forming tube.

Whilst the sealing mechanism is sealing the end of that bale and the start of the next bale, the ejection ram will return to the home position, as will the gate.  The compression ram will also return to the home position and, if the infrared sensor is covered, stroke forward and compress another bale.  This operation is completely fully automatic and is controlled by a Siemens programmable controller mounted in the machine control panel and the weights of each bale are displayed on the Siemens touch screen.

If adjustment of the bale weight is required, this can be done by a simple operation of the Siemens touch screen that displays the weights. Although this machine weighs every bale once it is made and adjusts the machine to suit if the bale is too heavy or too light the weight can be adjusted mid stroke using the touch screen.

This will not require constant adjustment but is a useful feature when installed on a ‘direct’ mill system to cope with the variance in sawdust content as machines stop and restart after setting.

# BALE - PAK BP-120/P fully automatic baler - 30 kw

## TECHNICAL SPECIFICATIONS

CAPACITY	3 bales per minute

MOTOR SIZE	30 kW (40HP)

MOTOR VOLTAGE	415 V  3 PH  50 HZ

CONTROL VOLTAGE	110 V

HYDRAULIC TANK CAPACITY	1025 Its (225gals)

MAXIMUM THRUST	48 Tonnes

FEED OPENING	720 x 1600

BALE SIZE	350 x 430 x 750

BALE WEIGHT	22 - 25 KGs

MAIN COMPRESSION RAM	150 Bore x 1830 Stroke

EJECTION RAM	100 Bore x 3000 Stroke

GATE RAM	80 Bore x 270 stroke

DRY WEIGHT OF MACHINE	4000 KGs

# BALE - PAK BP-120/P fully automatic baler - 45 kw

## TECHNICAL SPECIFICATIONS

CAPACITY	4 bales per minute

MOTOR SIZE	45 kW (60HP)

MOTOR VOLTAGE	415 V  3 PH  50 HZ

CONTROL VOLTAGE	110 V

HYDRAULIC TANK CAPACITY	1230 Its (270gals)

MAXIMUM THRUST	48 Tonnes

FEED OPENING	720 x 1600

BALE SIZE	350 x 430 x 750

BALE WEIGHT	22 - 25 KGs

MAIN COMPRESSION RAM	150 Bore x 1830 Stroke

EJECTION RAM	100 Bore x 3000 Stroke

GATE RAM	80 Bore x 270 stroke

DRY WEIGHT OF MACHINE	4000 KGs